Path Planning Project
Udacity Self Driving Nanodegree
Path Planning

Reflections:

1. Speed Control:
To avoid jerks, the simulator uses incremental steps to increase and decrease vehicle speed. Speed is increased or decreased by 0.224 mph every 0.02 sec (Simulator operation frequency is 50 Hz). In case of no car ahead within 20 m, the speed is increased until 49.5 mph.

Speed is decreased as soon as the car in front comes in within 20 meter range by 0.224 mph every 0.02 sec which is increased to 0.448 mph every 0.02 seconds if it comes within 7 meter range.

2. Waypoints:

a. Path planner output:	50 x, y points are passed to the simulator as desired set points. These are final output of path planner in Cartesian co-ordinate system in car’s local co-ordinate system.

b. Generating paths:
The simulator sends list of previous path points (waypoints) which are yet to be realized. The last two points from previous path are taken as starting points to plan for next points.

Next points: In Frenet co-ordinates, 3 points are generated at 30 m apart at target lane from the ‘starting points’ to be planned described earlier. The points are converted to Cartesian co-ordinate system & shifted to car local co-ordinate system before adding to new path points. Decision of target lane is described in the next section. New path points now has total 5 points.

Spline C++ library is used to fit smooth curve to the new path points. A target of 30 m distance is used to calculate new path points every 0.02 seconds using the spline curve calculated earlier. These new points are added to previous path points which still need to be realized until there are total 50 points.

(Note: 30 m is sufficient since at maximum speed (50 mph), it takes 67 steps of 0.02 seconds. This ensures we always have path points more than 50).

Lane change is taken care of by path points since the spline curve generated used a ‘target lane’ and 3 equidistant points of 30 m in Frenet co-ordinates. Thus if current lane is 1 and target is 2, the path is planned from distance 0m, lane 1 to distance 30m, lane 2 and next distances with lane 2. This takes care of lateral jerk requirement in the project.

3. Lane change strategy:
 The goal is to decide the lane number to maintain higher vehicle speed. Lane change calculations are only executed if the car in front is within a certain distance (30 m). Lane safety is checked for right lane change and left change based on cars in respective lanes.

Lane safety criteria: The car lane change can be either left or right. For each case, sensor fusion data is analyzed to check cars in target lane (left/right).

To be safe for lane change, first criterion is that there should not be any cars within +- 4m. In addition, the distances of cars in target lane are predicted in the time it takes our car to finish lane change maneuver. If all cars in target lane are more than 20 m away in front and more than 5 m behind our predicted distance after predicted lane change, lane change is safe.

If both left lane change and right lane change are safe, lane is decided based on which one has more predicted buffer with the immediate car in front. In case of a tie, left lane change is preferred. At extremes of the highway, there is only one option for lane change.

When a lane change is active, calculation of lane change is frozen to prevent lane toggling during a lane change.
4. Conclusion:

The car completes the track without any incidence. Further improvements can be made by implementing prediction module, behavior planner & trajectory module to generalize the solution to broader scenarios.